## Slide 1: Introduction to Assembly Language
Lecture 1

## Slide 2: Basic Computer Architecture

## Slide 3: Components of Digital Computer
Computer uses these components in order to provide different functionalities (programs):
Memory stores program and data (input, output and intermediate data)
Central Processing Unit (CPU)
  Performs Operations
  Arithmetic Logic Unit (ALU) performs arithmetic and data-processing operations as specified by program
  Control Unit supervises the flow of information between the various units
  ALU and Control Unit together form CPU
  Input Devices such as Mouse, Keyboard, DVD drives, CD-ROM, Microphones, Scanner, Webcam etc. are used to take data input in programs
  Output Devices such as LCD, Printer and Loudspeakers etc. are used to present result to the user

## Slide 4: Microcomputer Block Diagram
Design of Simple 4-bit Processor
Wires where CPU provides Address
Wires where Data travels for read and write
Read or Write Signal

## Slide 5: A Simple Program
A=15
B=12
C=5
D=10
D = D+C
A = A-C
B = B x C
…
How the processor executes this program?
Can you design a simple processor to execute this piece of code?

## Slide 6: Simple Processor
Program |  | A | B | C | D
 |  | 0 | 0 | 0 | 0
A = 15 |  |  |  |  | 
B = 12 |  |  |  |  | 
C = 5 |  |  |  |  | 
D = 10 |  |  |  |  | 
D = D+C |  |  |  |  | 
A = A-C |  |  |  |  | 
B = B x C |  |  |  |  | 
… |  |  |  |  | 
How the processor initializes all the data to zero?
Data Assignment?
Can you implement this processor?
Writing on one of n memory cells?

## Slide 7: Simple Processor
Program |  | A | B | C | D
 |  | 0 | 0 | 0 | 0
A = 15 |  | 15 | 0 | 0 | 0
B = 12 |  | 15 | 12 | 0 | 0
C = 5 |  | 15 | 12 | 5 | 0
D = 10 |  | 15 | 12 | 5 | 10
D = D+C |  |  |  |  | 
A = A-C |  |  |  |  | 
B = B x C |  |  |  |  | 
… |  |  |  |  | 
How the processor initializes all the data to zero?
Data Assignment?
Can you implement this processor?
Writing on one of n memory cells?
Notes: D = D + C
A = A + B
C = C + D

## Slide 8
A
B
C
D
Operand 1
4x1
Quad
MUX
Binary of
Operand 1
A
B
C
D
Operand 2
4x1
Quad
MUX
Binary of
Operand 2
Adder
X
Y
X+Y
What important signals do we need for
D = D + C
A = A + C
A = A + B
Notes: D = D + C
A = A + B
C = C + D

## Slide 9
A
B
C
D
Operand 1
4x1
Quad
MUX
Binary of
Operand 1
A
B
C
D
Operand 2
4x1
Quad
MUX
Binary of
Operand 2
Adder
X
Y
X+Y
What about
D = D x C
A = A - C
A = A x B
Notes: A = A + C
A = A – C
A = A x C

## Slide 10
Adder
Subtractor
Multiplier
User Input
A
B
C
D
Op1
4x1
Quad
MUX
Binary of
Operand 1
A
B
C
D
Op2
4x1
Quad
MUX
Binary of
Operand 2
Op1
Op2
Op1
Op2
Op1
Op2
Op1 + Op2
Op1 - Op2
Op1 x Op2
What about following?
A = 10 (00)
A = A + C (01)
A = A – C (10)
A = A x B (11)
Notes: A = B x C, Op1 = (01) , Op2 = 10, Operation Multiply = (10), Dest Reg = (00)
A = 10

## Slide 11
Result of Adder
Data to be updated
4x1
Quad
MUX
Binary of
Operation
Result of Subtractor
Result of Multiplier
User Input
What about following?
A = A + C (00)
A = A – C (01)
A = A x B (10)
A = 10 (11)

## Slide 12
Data to be updated
4x1
Quad
MUX
Binary of
Operation
Adder
Subtractor
Multiplier
User Input
A
B
C
D
Op1
4x1
Quad
MUX
Binary of
Operand 1
A
B
C
D
Op2
4x1
Quad
MUX
Binary of
Operand 2
Op1
Op2
Op1
Op2
Op1
Op2
11
10
00
What about following?
A = A + C (00)
A = A – C (01)
A = A x B (10)
A = 10 (11)
01
Notes: A = B x C, Op1 = (01) , Op2 = 10, Operation Multiply = (10), Dest Reg = (00)
A = 10

## Slide 13
Data to be updated
4x1
Quad
MUX
Binary of
Operation
Reg A
Reg B
Reg C
Reg D
Adder
Subtractor
Multiplier
User Input
A
B
C
D
Op1
4x1
Quad
MUX
Binary of
Operand 1
A
B
C
D
Op2
4x1
Quad
MUX
Binary of
Operand 2
Op1
Op2
Op1
Op2
Op1
Op2
A
B
C
D
2x4
Decoder
Clks for Destination Reg
Binary for Destination Reg
11
10
00
Notes: A = B x C, Op1 = (01) , Op2 = 10, Operation Multiply = (10), Dest Reg = (00)
A = 10

## Slide 14: Microcomputer Block Diagram
Design of Simple 4-bit Processor
Wires where CPU provides Address
Wires where Data travels for read and write
Read or Write Signal

## Slide 15: Address Bus
How Processor reads or write one out of n registers?
How Processor will read/write one cell out of 4 Bytes Memory?
How Processor will read/write one cell out of 16 Bytes Memory?
How Processor will read/write one cell out of 1MB Memory?
Data
CPU
Address | Content
00 | 
01 | 
10 | 
11 | 
4 Bytes
Memory
Address
Data
CPU
Address | Content
0000 | 
0001 | 
0010 | 
0011 | 
… | 
1111 | 
16 Bytes
Memory
Address
What is the size of each Address Bus?

## Slide 16: Address Bus
When a processor needs to read or write to a memory location, it specifies that memory location on the address bus (the value to be read or written is sent on the data bus).
Unidirectional – Address always travels from processor to memory.
An address bus is a computer bus (a series of lines/wires connecting two or more devices) that is used to specify a physical address.
The CPU uses the address bus to select the desired memory or I/0 device by providing a unique address that corresponds to one of the many memory or I/0 elements in the system.

## Slide 17: Address Bus…
The number of address bus lines varies from one microcomputer to another.
The width of the address bus determines the amount of memory a system can address.
For example, a system with a 32-bit address bus can address 232 memory locations.
If each memory location holds one byte, the addressable memory space is 4 GB (=2^2 x 2^30 Bytes).

## Slide 18: Data Bus
What will be the size of data bus, for each of the following Memory configurations, if we want to read/write
  2 Bytes per read/write operation?
  4 Bytes per read/write operation?
Data
CPU
Address | Content
00 | 
01 | 
10 | 
11 | 
4 Bytes
Memory
Address
Data
CPU
Address | Content
0000 | 
0001 | 
0010 | 
0011 | 
… | 
1111 | 
16 Bytes
Memory
Address
What is the size of each Data Bus?
Notes: CPU will give the base address to read/write m bytes.

## Slide 19: Data Bus
The data bus is the set of wires over which data passes between the CPU and the memory and I/0.
Bidirectional
The data can either be instructions for the CPU, or information the CPU is passing to or from I/0 ports.
Best and simplest operation requires the same size of data bus and memory cell width.
From one microcomputer to another, the number of bus lines may vary.
Notes: Reference: iAPX 88 Book s-2
Data Bus = 4 Bits, 32 Bits,
Memory Size => 4 Bytes
2^20

## Slide 20: Test you concepts
Given following specifications, determine the size of Data Bus and Address Bus:
  A 64-Bit Machine with 2GB Memory
  A 32-Bit Machine with 64MB Memory
  A 16-Bit Machine with 1MB Memory (iAPX88)
Notes: 2 GB - 2^30 Bytes ….. 2^30 Cell……
Address Bus Size  30 Lines
64MB = 64x2^20 Cells = 2^26 Cells
1MB = 1 Mega Bytes

## Slide 21: Test you concepts
  What are Specifications of following system?
Notes: 2 GB - 2^30 Bytes ….. 2^30 Cell……
Address Bus Size  30 Lines
64MB = 64x2^20 Cells = 2^26 Cells
1MB = 1 Mega Bytes

## Slide 22: Control Bus
Control bus carries commands from the CPU and returns status signals from the devices.
For example, if the data is being read or written to the device the appropriate line (read or write) will be active (logic one).
Implementation of System Bus?
Notes: Reference: iAPX 88 Book s-2

## Slide 23: Read Data from Memory Cell no 2453
Notes: - CPU sends out the address value 2453 on the address bus
- CPU sends out the signal R/W = 1 on the control bus, which indicates a READ operation
- CPU then waits for the data from memory on the data bus
- The R/W = 1 signal and the address bus value 2453 will cause the memory to retrieve the value at memory location 2453 to be sent out on the data bus
Reference: http://www.mathcs.emory.edu/~cheung/Courses/255/Syllabus/4-intro/mem-access.html

## Slide 24: Write 53 on Memory Cell no 2453
Notes: -CPU sends out the address value 2453 on the address bus
-CPU also sends out the value 53 on the data bus
-CPU now sends out the signal R/W = 0, which indicating a WRITE operation
-The R/W = 0 signal along with the address bus value 2453 and data bus value 53 will cause the memory to store the value 53 at the location 2453...
Reference: http://www.mathcs.emory.edu/~cheung/Courses/255/Syllabus/4-intro/mem-access.html

## Slide 25: Another Read/Write Operation

## Slide 26: Instruction Set
Operation Code | Operation Performed | Description
000 | R1 = Input A | Load the contents of input A in to the register operand 1 (R1).
001 | R1 = R2 | Move the contents of register operand 2 in to register operand 1.
010 | R1 = R1 + R2 | Add the contents of register operand 1 and register operand 2 and load in register operand 1.
011 | R1 = R1 - R2 | Subtract the contents of register operand 2 from register operand 1 and load in register operand 1.
100 | R1 = R1 * R2 | Multiply the contents of register operand 1 and register operand 2 and load in register operand 1 and 2. (As the result is of 8 bits)
101 | R1 = R1/2i | Divide the register contents of register operand 1 with 2i (i is an input) and load the result in register operand 1.
110 | R1 = R1*2I | Multiply the register contents of register operand 1 with 2i (i is an input) and load the result in register operand 1.
111 | R1 = R1 + R2 | Logical OR the contents of register operand 1 and register operand 2 and load in register operand 1.
I6-I4 | I3-I2 | I1 – I0
Operation Code | 4-bit register operand 1(R1) | 4-bit register operand 2 (R2)
Notes: an instruction set architecture (ISA) is an abstract model of a computer

## Slide 27: Executing Program on 4-Bit Simple Processor
High Level Language Code | Machine Code | A | B | C | D
 |  | 0 | 0 | 0 | 0
A = 15 | 000 00 XX |  |  |  | 
B = 12 |  |  |  |  | 
C = 5 |  |  |  |  | 
D = 10 |  |  |  |  | 
D = D+C |  |  |  |  | 
A = A-C |  |  |  |  | 
B = B x C |  |  |  |  | 
… |  |  |  |  | 

## Slide 28: Executing Program on 4-Bit Simple Processor…
High Level Language Code | Machine Code | A | B | C | D
 |  | 0 | 0 | 0 | 0
A = 15 | 000 00 XX |  |  |  | 
B = 12 | 000 01 XX |  |  |  | 
C = 5 |  |  |  |  | 
D = 10 |  |  |  |  | 
D = D+C |  |  |  |  | 
A = A-C |  |  |  |  | 
B = B x C |  |  |  |  | 
… |  |  |  |  | 

## Slide 29: Executing Program on 4-Bit Simple Processor…
High Level Language Code | Machine Code | A | B | C | D
 |  | 0 | 0 | 0 | 0
A = 15 | 000 00 XX |  |  |  | 
B = 12 | 000 01 XX |  |  |  | 
C = 5 | 000 10 XX |  |  |  | 
D = 10 | 000 11 XX |  |  |  | 
D = D+C |  |  |  |  | 
A = A-C |  |  |  |  | 
B = B x C |  |  |  |  | 
… |  |  |  |  | 

## Slide 30: Executing Program on 4-Bit Simple Processor…
High Level Language Code | Machine Code | A | B | C | D
 |  | 0 | 0 | 0 | 0
A = 15 | 000 00 XX |  |  |  | 
B = 12 | 000 01 XX |  |  |  | 
C = 5 | 000 10 XX |  |  |  | 
D = 10 | 000 11 XX |  |  |  | 
D = D+C | 010 11 10 |  |  |  | 
A = A-C |  |  |  |  | 
B = B x C |  |  |  |  | 
… |  |  |  |  | 

## Slide 31: Executing Program on 4-Bit Simple Processor…
High Level Language Code | Machine Code | A | B | C | D
 |  | 0 | 0 | 0 | 0
A = 15 | 000 00 XX |  |  |  | 
B = 12 | 000 01 XX |  |  |  | 
C = 5 | 000 10 XX |  |  |  | 
D = 10 | 000 11 XX |  |  |  | 
D = D+C | 010 11 10 |  |  |  | 
A = A-C | 011 00 10 |  |  |  | 
B = B x C |  |  |  |  | 
… |  |  |  |  | 

## Slide 32: System Bus

## Slide 33: System Bus…
A peripheral or peripheral device is "an ancillary device used to put information into and get information out of the computer"

## Slide 34: Homework
History of Processors
Processor specifications of your Personal Computer and Smart Phone

## Slide 35: References
Chapter 1 of Lecture Notes (1.1 to 1.6)
iAPX88 Manual
http://www.mathcs.emory.edu/~cheung/Courses/255/Syllabus/4-intro/mem-access.html