## Slide 1: Segmented Memory Model
Lecture – 13

## Slide 2: Segmented Memory Model
Offset Registers: BX, SI, DI, BP, SP, IP
Offset Register contains address of data (or instruction)
[BX], [SI], [DI] to access (i.e. read/write) data
[IP] is next instruction/opcode
Size of offset registers = 16-bit OR 2 Byte (1 Word)
Minimum address possible in offset register
Maximum address possible in offset register
Range of Offset Register: 0000 to FFFF
Total memory space offset register can cover = 216 = 26 x210 = 64KB
This memory space is called Segment.
X | X | X | X
0 | 0 | 0 | 0
F | F | F | F

## Slide 3: Segmented Memory Model…
Maximum Memory iAPX 88 can access is 1 MB
Bits required to access 1MB Memory is 20 bits
1MB = 1 Mbytes = 2^20 Bytes  20 Lines required to access 2^20 Bytes
Actual Physical Memory Addresses 00000 to FFFFF.
If we are writing at [BX],where BX = 0x103, where actually [0x103] is writing?
Problem: We are using 16-bits (BX) to access memory while Physical Memory address is of 20-bits.
Solution: This is actually [DS:BX] i.e. [DS : 0x0103]
X | X | X | X
Max Register Size 16 Bits |  |  | 
BX |  |  | 
0 | 1 | 0 | 3
Z | Z | Z | Z | Z
Physical Address 20 Bits |  |  |  | 
DS |  |  | 
1 | 9 | F | 5

## Slide 4: Segmented Memory Model…
Segment Registers: CS, DS, SS, ES
Offset Registers: BX, SI, DI, BP, SP, IP
Default Segment Association:
[IP] is actually (by default) [CS : IP]
[SI], [DI], [BX] are actually (by default) [DS : SI], [DS : DI], [DS : BX]
[BP], [SP] are actually (by default) [SS : BP], [SS : SP]
[defaultSegmentOfBase : base+index(+constant)]
To override association (if required) for one instruction: [ES:DI], after execution of this line DI is back to default association

## Slide 5: Logical to Physical Address Mapping
Y | Y | Y | Y
Segment Register |  |  | 
X | X | X | X
Offset Register |  |  | 
Logical/Effective Address:
Segment-Offset pair
[Segment : Offset]
[YYYY : XXXX ]
E.g. [DS:BX] [19F5:0103], [SS:SP] [19F5:FFFE]
Physical Address:
YYYY0 ;(Append 0 at the end of Segment Value)
0XXXX + ;(Append 0 at the start of Offset Value)
-------------
ZZZZZ (20-bit Physical Address)

## Slide 6: Logical to Physical Address Mapping
Y | Y | Y | Y
Segment Register |  |  | 
X | X | X | X
Offset Register |  |  | 
Logical/Effective Address:
Segment-Offset pair
[Segment : Offset]
[YYYY : XXXX ]
E.g. [DS:BX] [19F5:0103], [SS:SP] [19F5:FFFE]
Physical Address:
YYYY0
0XXXX +
-------------
ZZZZZ (20-bit Physical Address)
Example: If BX=0x0103, where is [BX] writing?  [DS:BX]
[19F5: 0103]  Logical Address
19F50
00103
---------
1A053  Physical Address

## Slide 7: Logical to Physical Address Mapping
Y | Y | Y | Y
Segment Register |  |  | 
X | X | X | X
Offset Register |  |  | 
Logical/Effective Address:
Segment-Offset pair
[Segment : Offset]
[YYYY : XXXX ]
E.g. [DS:BX] [19F5:0103], [SS:SP] [19F5:FFFE]
Physical Address:
YYYY0
0XXXX +
-------------
ZZZZZ (20-bit Physical Address)
Example: Where first call/push writes on stack?  FFFE  [SS:SP]
[19F5: FFFE]  Logical Address
19F50
0FFFE
---------
29F4E  Physical Address
Notes: 29F4E , 19F4 : offset

## Slide 8: Exploring Segment No. 0000
Segment Registers: CS, DS, SS, ES
All possible Offsets with Segment 0000:
0000:0000
0000:0001
0000:0002
…
0000:FFFF
All Segment:Offset Pairs of Segment = 0000
Range of Segment 0000 is from Byte# 0000 to FFFF
i.e. 0 to 65535 i.e. total 65536 Bytes i.e. 64KBs
0000 : 0000
0000 : 0001
0000 : 0002
…
0000 : 0009
0000 : 000A
…
0000 : 000F
…
0000 : FFFF
1 MB Memory

## Slide 9: Exploring Segment No. 0001 (No-Overlap)
Segment Registers: CS, DS, SS, ES
All possible Offsets with Segment 0001:
0001:0000
0001:0001
0001:0002
…
0001:FFFF
How many non-overlapping Segments required for 1MB memory if one segment is of 64 KB?
If size of Offset Register is 20bits, do we need Segment-Offset Pair to access whole Physical Memory?
0000 : 0000
0000 : 0001
0000 : 0002
…
0000 : 0009
0000 : 000A
…
0000 : 000F
…
0000 : FFFF
0001 : 0000
0001 : 0001
0001 : 0002
…
0001 : 0009
0001 : 000A
…
0001 : 000F
…
0001 : FFFF
1 MB Memory
Notes: 2^20 / 2^16 = 2^4
10 / 2 = 5

## Slide 10: Exploring Addresses
Segment Registers: CS, DS, SS, ES
All possible values of a Segment Register:
0000, 0001, 0002, … , 0009, 000A,000B,…, 000F, …, FFFF
So a segment number can be:
0000, 0001, 0002, … , 0009, 000A,000B,…, 000F, …, FFFF
Notes: 2^16

## Slide 11: Overlapping Segments
Logical Address [0000:0010]  Physical Address?
Logical Address [0001:0000]  Physical Address?
1 MB Memory

## Slide 12: Overlapping Segments
Logical Address [0000:0010]  Physical Address?
Logical Address [0001:0000]  Physical Address?
1 MB Memory
00000
00010 +
--------------
00010 (What Byte No. is this in Memory?)

## Slide 13: Overlapping Segments
Logical Address [0000:0010]  Physical Address?
Logical Address [0001:0000]  Physical Address?
Byte # 0
00001
00002
…
00009
0000A
0000B
…
0000F
00010 = [0000:0010]
1 MB Memory
00000
00010 +
--------------
00010 (This is Byte # 16 in Memory)

## Slide 14: Overlapping Segments
Logical Address [0000:0010]  Physical Address?
Logical Address [0001:0000]  Physical Address?
1 MB Memory
00010
00000 +
--------------
00010 (This is also Byte # 16 in Memory)
Byte # 0
00001
00002
…
00009
0000A
0000B
…
0000F
00010 = [0000:0010] = [0001:0000]

## Slide 15: Overlapping Segments
Logical Address [0000:0010]  Physical Address?
Logical Address [0001:0000]  Physical Address?
1 MB Memory
00010
00000 +
--------------
00010 (This is also Byte # 16 in Memory)
What about [0000:0011] and [0001:0001]? Calculate Physical addresses of these Logical Addresses and check.
Byte # 0
00001
00002
…
00009
0000A
0000B
…
0000F
00010 = [0000:0010] = [0001:0000]

## Slide 16: Overlapping Segments
Logical Address [0000:0010]  Physical Address?
Logical Address [0001:0000]  Physical Address?
1 MB Memory
00010
00000 +
--------------
00010 (This is also Byte # 16 in Memory)
We have overlapping segments i.e. Different segments are sharing cells using different (Segment, Offset) Pairs.
Byte # 0
00001
00002
…
00009
0000A
0000B
…
0000F
00010 = [0000:0010] = [0001:0000]

## Slide 17: Overlapping Segments
Range of Segment # 0000:
[0000 : 0000] to [0000 : FFFF]
Find Corresponding Physical Addresses.
1 MB Memory
Byte # 0
00001
00002
…
00009
0000A
0000B
…
0000F
00010 = [0000:0010] = [0001:0000]
00000
00000 +
--------------
00000 (First Byte of Segment 0000)
00000
0FFFF +
--------------
0FFFF (Last Byte of Segment 0000)
Where is this in Memory?

## Slide 18: Overlapping Segments
Range of Segment # 0001:
[0001 : 0000] to [0001 : FFFF]
Find Corresponding Physical Addresses.
1 MB Memory
Byte # 0
00001
00002
…
00009
0000A
0000B
…
0000F
00010 = [0000:0010] = [0001:0000]
00010
00000 +
--------------
00010 (First Byte of Segment 0001)
00010
0FFFF +
--------------
1000F (Last Byte of Segment 0001)
Where is this in Memory?

## Slide 19: Overlapping Segments
Range of Segment # 0000:
Logical Address: [0000 : 0000] to [0000 : FFFF]
Physical Address: 00000 to 0FFFF
Range of Segment # 0001:
[0001 : 0000] to [0001 : FFFF]
Physical Address: 00010 to 1000F
Overlap:
Physical Address: 00010 to 0FFFF
(Except first and last 16 bytes, all the bytes are shared i.e. overlap)
1 MB Memory
Byte # 0
00001
00002
…
00009
0000A
0000B
…
0000F
00010 = [0000:0010] = [0001:0000]

## Slide 20: Address Wraparound
Range of Segment # FFFF:
[FFFF : 0000] to [FFFF : FFFF]
Find Corresponding Physical Addresses.
1 MB Memory
Byte # 0
00001
00002
…
00009
0000A
0000B
…
0000F
00010 = [0000:0010] = [0001:0000]
FFFF0
00000 +
--------------
FFFF0 (First Byte of Segment FFFF)
FFFF0
0FFFF +
--------------
0FFEF (Last Byte of Segment FFFF, Just keep 20-bits answer)
Where is this in Memory?

## Slide 21: Address Wraparound
Range of Segment # FFFF:
[FFFF : 0000] to [FFFF : FFFF]
Corresponding Physical Addresses: FFFF0 to 0FFEF
1 MB Memory
Byte # 0
00001
00002
…
00009
0000A
0000B
…
0000F
00010 = [0000:0010] = [0001:0000]
Segment # FFFF starts from last 16 Bytes of Memory and covers remaining bytes of 64KB from start
i.e. it covers addresses FFFF0, FFFF1, FFFF2, …, FFFF9, FFFFA, FFFFB,…,FFFFF, 00000, 00001, … , 0FFEF.
Question: Which Byte # (or Physical Addresses) are [FFFF:0010], [FFFF:0011] and [FFFF:0020]?

## Slide 22: Jumps
1 ; a program to add ten numbers without a separate counter
2 [org 0x0100]
3 00000000 E91600 jmp start ; unconditionally jump over data
4 00000003 0A0014001E00280032- num1: dw 10, 20, 30, 40, 50, 10, 20, 30, 40, 50
5 0000000C 000A0014001E002800-
6 00000015 3200
7 00000017 0000 total: dw 0
8
9 00000019 BB0000 start: mov bx, 0 ; initialize array index to zero
10 0000001C B80000 mov ax, 0 ; initialize sum to zero
11
12 0000001F 0387[0300] l1: add ax, [num1+bx] ; add number to ax
13 00000023 81C30200 add bx, 2 ; advance bx to next index
14 00000027 81FB1400 cmp bx, 20 ; are we beyond the last index
15 0000002B 75F2 jne l1 ; if not add next number
16
17 0000002D A3[1700] mov [total], ax ; write back sum in memory
18 00000030 B8004C mov ax, 0x4c00 ; terminate program
19 00000033 CD21 int 0x21

## Slide 23: Jumps…
1 ; 4bit multiplication algorithm
2 [org 0x100]
3 00000000 E90300 jmp start
4
5 00000003 0D multiplicand: db 13 ; 4-bit multiplicand (8-bit space)
6 00000004 05 multiplier: db 5 ; 4-bit multiplier
7 00000005 00 result: db 0 ; 8-bit result
8
9 00000006 B104 start: mov cl, 4 ; initialize bit count to four
10
11 00000008 8A1E[0300] mov bl, [multiplicand] ; load multiplicand in bl
12 0000000C 8A16[0400] mov dl, [multiplier] ; load multiplier in dl
13
14 00000010 D0EA checkbit: shr dl, 1 ; move right most bit in carry
15 00000012 7304 jnc skip ; skip addition if bit is zero
16 00000014 001E[0500] add [result], bl ; accumulate result
17
18 00000018 D0E3 skip: shl bl, 1 ; shift multiplicand left
19 0000001A FEC9 dec cl ; decrement bit count
20 0000001C 75F2 jnz checkbit ; repeat if bits left
21
22 0000001E B8004C mov ax, 0x4c00 ; terminate program
23 00000021 CD21 int 0x21

## Slide 24: Jumps…
1 ; 4bit multiplication algorithm
2 [org 0x100]
3 00000000 E90300 jmp start
4
5 00000003 0D multiplicand: db 13 ; 4-bit multiplicand (8-bit space)
6 00000004 05 multiplier: db 5 ; 4-bit multiplier
7 00000005 00 result: db 0 ; 8-bit result
8
9 00000006 B104 start: mov cl, 4 ; initialize bit count to four
10
11 00000008 8A1E[0300] mov bl, [multiplicand] ; load multiplicand in bl
12 0000000C 8A16[0400] mov dl, [multiplier] ; load multiplier in dl
13
14 00000010 D0EA checkbit: shr dl, 1 ; move right most bit in carry
15 00000012 7304 jnc skip ; skip addition if bit is zero
16 00000014 001E[0500] add [result], bl ; accumulate result
17
18 00000018 D0E3 skip: shl bl, 1 ; shift multiplicand left
19 0000001A FEC9 dec cl ; decrement bit count
20 0000001C 75F2 jnz checkbit ; repeat if bits left
21 0000001E E9EFFF jmp checkbit
22 00000021 E9F4FF jmp skip
23
24 00000024 B8004C mov ax, 0x4c00 ; terminate program
25 00000027 CD21 int 0x21

## Slide 25: Near Jump
Opcode YYYY (16-bit Signed offset given)
- New IP = IP + YYYY
Jump within a segment
Examples:
  00000000 E91600
  00000000 E90300

## Slide 26: Short Jump
Opcode YY (8-bit Signed Offset)
New IP = IP + YY
Range of Short Jump: +127 (0111 1111) to -128 (1000 0000) Bytes
Jump within a segment

## Slide 27: Far Jump
Jump to new CS:IP values