## Slide 1: Real Time Interrupts and Hardware Interfacing
Textbook - Chapter 9

## Slide 2: Interrupt:
“An interrupt is an input signal to the processor indicating an event that needs immediate attention.”
Interrupts are Events that occur outside the processor and the processor must be informed about them

## Slide 3: Interrupt Handler (ISR)
“The Routine that executes in response to an INT instruction is called the Interrupt Service Routine (ISR) or Interrupt Handler”
ISR is just a piece of code (list of instructions) or program residing somewhere in memory.
For example, KeyboardISR, is handling all the keys and showing you different screens/functionalities for different combinations i.e Ctrl+Alt+Del, WindowsKey+D, Esc, Ctrl+C, Ctrl+V etc.
….
KeyboardISR: …
…
….
MouseISR: …
…
….
USBISR: …
…
00000
FFFFF
0ABCD
0BCDE
0CDEF

## Slide 4: Hardware Interrupts
External devices that need to communicate with processor: keyboard, hard disk, floppy disk, sound card etc.
If more than one interrupt comes at the same times, the highest priority one is forwarded and the rest are held till that is serviced.
The rest are forwarded one by one according to priority after the highest priority one is completed.
Programmable Interrupt Controller(PIC)
Programmable
Interrupt Controller
(PIC)
INT Pin
IRQ7
IRQ0
IRQ1
IRQ2
IRQ3
IRQ4
IRQ5
IRQ6
Timer
Keyboard
Parallel Port
Floppy Disk
Sound Card/
Network Card/
Modem
Serial Port
COM1
Serial Port
COM2
…
Notes: For example if a program is busy in some calculations for three minutes the key strokes that are hit meanwhile should not be wasted. Therefore when a key is pressed, the INT signal is sent, an interrupt generated and the interrupt handler stores the key for later use. Similarly when the printer is busy printing we cannot send it more data. As soon as it gets free from the previous job it interrupts the processor to inform that it is free now.

## Slide 5: Hardware Interrupts
Interrupt Request (IRQ)
IRQ 0 to IRQ 7
Programmable
Interrupt Controller
(PIC)
INT Pin
IRQ7
IRQ0
IRQ1
IRQ2
IRQ3
IRQ4
IRQ5
IRQ6
Timer
Keyboard
Parallel Port
Floppy Disk
Sound Card/
Network Card/
Modem
Serial Port
COM1
Serial Port
COM2
…

## Slide 6: Hardware Interrupts
an interrupt request from a device enters the PIC as an IRQ
from there it reaches the INT pin of the processor
the processor receives the interrupt number from the PIC
generates the designated interrupt, and finally the interrupt handler gain control and can do whatever is desired
At the end of servicing the interrupt the handler should inform the PIC that it is completed so that lower priority interrupts can be sent from the PIC. This signal is called an End Of Interrupt (EOI) signal and is sent through the I/O ports of the interrupt controller
Programmable
Interrupt Controller
(PIC)
INT Pin
IRQ7
IRQ0
IRQ1
IRQ2
IRQ3
IRQ4
IRQ5
IRQ6
Timer
Keyboard
Parallel Port
Floppy Disk
Sound Card/
Network Card/
Modem
Serial Port
COM1
Serial Port
COM2
…

## Slide 7: Hardware Interrupts
How many external devices are communicating with your processor?
Interrupt Request (IRQ)
Programmable Interrupt Controller (PIC)
Single pin outside the processor (INT Pin) is used by external hardware to generate interrupts
End of Interrupt (EOI) Signal
Interrupts Priority
Programmable
Interrupt Controller
(PIC)
INT Pin
IRQ7
IRQ0
IRQ1
IRQ2
IRQ3
IRQ4
IRQ5
IRQ6
Timer
Keyboard
Parallel Port
Floppy Disk
Sound Card/
Network Card/
Modem
Serial Port
COM1
Serial Port
COM2
…

## Slide 8: Interrupt Mapping
Programmable
Interrupt Controller
(PIC)
INT Pin
IRQ7
IRQ0
IRQ1
IRQ2
IRQ3
IRQ4
IRQ5
IRQ6
Timer
Keyboard
Parallel Port
Floppy Disk
Sound Card/
Network Card/
Modem
Serial Port
COM1
Serial Port
COM2
…
Interrupt Request | INT#
IRQ 0 | INT 8
IRQ 1 | INT 9
IRQ 2 | INT A
IRQ 3 | INT B
IRQ 4 | INT C
IRQ 5 | INT D
IRQ 6 | INT E
IRQ 7 | INT F
Timer tick comes 18.2 times per second
i.e. after every 55ms
Timer is highest priority interrupt.
Notes: Examples: Printer, Keyboard

## Slide 9: Reading Assignment
Chapter 9
  9.1
  9.2

## Slide 10: I/O Ports
Peripheral Devices: Keyboard, sound card, network card, PIC etc.
To communicate with peripheral devices (read or write data), processor uses I/O ports
Port Numbers: PIC (20, 21), Keyboard (60 to 64), Parallel Port (378)
Communication: Read or write I/O port
Same Address and data buses are used to read/write data from port
Read data from a Port
in al, 0x21
mov dx, 0x378
In al, dx
Write data to a Port
out 0x21, al
mov dx, 0x378
out dx, al

## Slide 11: Example 9.1
; disable keyboard interrupt in PIC mask register
[org 0x0100]
in al, 0x21 ; read interrupt mask register
or al, 2 ; set bit for IRQ2
out 0x21, al ; write back mask register
mov ax, 0x4c00 ; terminate program
int 0x21

## Slide 12: Scan Code
Press Code vs Release Code
  Most Significant bit is clear in press code and set in release code

## Slide 13: Operations of Processor after getting Interrupt N
Which instruction will be executed next?
As soon as these values are loaded in CS and IP execution goes to the start of the interrupt handler or ISR of Nth interrupt.
…
Offset of Next Instruction
CS
FLAGS
Stack
Complete current Instruction
sp ← sp-2
[sp] ← flag (Save Current State)
if ← 0
tf ← 0
sp ← sp-2
[sp] ← cs
sp ← sp-2
[sp] ← ip
ip ← [0:N*4] (for Nth Interrupt)
cs ← [0:N*4+2]
CS:IP for Next Instruction
To be executed on return

## Slide 14: Interrupt and Trap Flags
Trap Flag (T) - The trap flag has a special role in debugging
Interrupt Flag (I) - It tells whether the processor can be interrupted from outside or not.

## Slide 15: After Execution of ISR
When the handler finishes its work it uses the IRET instruction to return to the caller.
ip ← [sp]
sp ← sp+2
cs ← [sp]
sp ← sp+2
flag ← [sp]
sp ← sp+2
ISRN: …
;Assembly Code Here
…
…
IRET ; Return from ISR
Sample ISR
…
Offset of Next Instruction
CS
FLAGS
Stack

## Slide 16: Memory Configuration before Hooking
Physical Memory Address | Memory Content
0:0 | INT 0 Handler (IP+CS)
… | 
0:36 | Default INT 9 Handler IP + CS ( F000 : E987 )
… | 
19F5:0100 | Jmp start
 | Message1: …
 | ….
19F5:0120 | Oldisr: 0:0
19F5:0124 | Kbisr:….
19F5:014B | Start:…
19F5:017D | int 0x21
 | …..
F000:E987 | … original keyboard handler ….

## Slide 17: Memory Configuration after Hooking
Physical Memory Address | Memory Content
0:0 | INT0 Handler (IP+CS)
… | 
0:36 | Default INT 9 Handler IP + CS (19F5:0124)
… | 
19F5:0100 | Jmp start
 | Message1: …
 | ….
19F5:0120 | Oldisr: ( F000 : E987 )
19F5:0124 | Kbisr:….
19F5:014B | Start:…
19F5:017D | int 0x21
 | …..
F000:E987 | … original keyboard handler ….

## Slide 18: Memory Configuration after Hooking
Physical Memory Address | Memory Content
0:0 | INT0 Handler (IP+CS)
… | 
0:36 | Default INT 9 Handler IP + CS (19F5:0124)
… | 
19F5:0100 | Jmp start
 | Message1: …
 | ….
19F5:0120 | Oldisr: ( F000 : E987 )
19F5:0124 | Kbisr:….
19F5:014B | Start:…
19F5:017D | int 0x21
 | …..
F000:E987 | … original keyboard handler ….

## Slide 19: Memory Configuration after loading new exe
Physical Memory Address | Memory Content
0:0 | INT0 Handler (IP+CS)
… | 
0:36 | Default INT 9 Handler IP + CS (19F5:0124)
… | 
19F5:0100 | Jmp start
 | Message1: …
 | ….
19F5:0120 | Oldisr: ( F000 : E987 )
19F5:0124 | 6C6F20776F72…
19F5:014B | Start:…
19F5:017D | …
19F5:0202 … | int 0x21 ….
F000:E987 | … original keyboard handler ….

## Slide 20: Other Concepts…
Key Press VS Key Released
  MSbit in Key Press scancode is 0
  MSbit in Key Release scancode is 1
Chaining VS Selective Chaining

## Slide 21: Terminate and Stay Resident (TSR)
DOS Service 4C VS 31
  FreeMem = FreeMem + X Bytes
1 Paragraph = 16 Bytes
337/16 = 21.1
337 + 15 = 352/16 = 22
FreeMem
Pointer (A)
Your
Code
Here
INT 21 - DOS 2+ - TERMINATE AND STAY RESIDENT
AH = 31h
AL = return code
DX = number of paragraphs to keep resident
X = 0x151
= (337)10
337/16 = 21.1
FreeMem
Pointer + 16

## Slide 22: Programmable Interval Timer
IRQ 0 is generated 18.2 times per second
One timer Tick after every 55ms